## Slide 1: Last-Level Cache Side-Channel Attacks are Practical
Fangfei Liu, Yuval Yarom, Qian Ge, Gernot Heiser, Ruby B. Lee Appeared in S&P'15
Presented by Baltasar Dinis and Rem Yang

## Slide 2: Side-channel attacks are hard to deploy
The L1i, L1d (and L2) caches are:
  Fast and small → high timing resolution → easier to attack
  Core-private, thus unlikely to be shared among cloud clients
Cloud providers disable page sharing between VMs
  This thwarts both FLUSH+RELOAD and EVICT+RELOAD attacks
LLC
L1
L1
DRAM

## Slide 3: Prime + Probe
Sets
Ways
Attacker
Victim

## Slide 4: Prime + Probe
Prime a cache set
Sets
Ways
Attacker
Victim

## Slide 5: Prime + Probe
Prime a cache set
Wait for some time
Sets
Ways
Attacker
Victim

## Slide 6: Prime + Probe
Prime a cache set
Wait for some time
Probe cache set
Sets
Ways
Attacker
Victim

## Slide 7: Prime + Probe
Victim did not access cache set
Attacker probe is fast
Sets
Ways
Attacker
Victim

## Slide 8: Prime + Probe
Victim did access cache set
Attacker probe is slow
Sets
Ways
Attacker
Victim
Evict

## Slide 9: Solving the "easy" challenges
Q: If the secret data is in the L1, how can we observe data accesses in the LLC?
A: Leverage the fact that the LLC is inclusive → evicting data in the LLC forces an eviction in the victim L1
Q: How to target specific cache sets in the LLC if it is physically indexed?
A: By using huge pages in the attacker code, all the set index bits are in the page offset (constant under address translation)
LLC
DRAM
L1
L1

## Slide 10: Prerequisite for PRIME+PROBE
Attacker needs to know which memory accesses map to the same cache set (the eviction set)
LLC
L1
L1
DRAM
Sets
Ways

## Slide 11: The LLC is sliced, and that's complicated
Each core is connected to a local slice of the LLC, use a ring bus to handle remote accesses
  Slice ID is computed from a hash of the address
The access latency varies with which slice we are targeting → we need to PRIME+PROBE within the same slice to get consistent time readings
L1
L1
LLC0
DRAM
LLC1

## Slide 12: PRIME+PROBE on the sliced LLC is hard
Attacker needs to know which memory accesses map to the same cache set and cache slice
Slice 1
Slice 0
Slice 2

## Slide 13: Constructing the Eviction Set
Goal: partition lines (in the same set) into per-slice eviction sets
For illustration, assume LLC has 2 ways and 2 slices
lines
eviction_set_0
eviction_set_1

## Slide 14: Constructing the Eviction Set
Construct the minimal group of lines that span the entire set across all slices
For each candidate in lines:
  If not conflicts with conflict_group:
    Move to conflict_group
lines
conflict_group
eviction_set_0
eviction_set_1

## Slide 15: Constructing the Eviction Set
lines
conflict_group
Partition the conflict_group by slice
For each candidate left in lines:
  Use it to distinguish members of the conflict_group; if they conflict, they belong to the same slice
eviction_set_0
eviction_set_1

## Slide 16: Attacking Square + Multiply Exponentiation
// compute b^e % mod
// e is secret
func sq_mul(b, mod, e):
r = 1
for i in len(e):
r = square(r) % mod
// secret dependent
if e_i == 1:
r = r * b % mod
return r
Repeatedly PRIME+PROBE the LLC
Observe intervals between cache accesses made by the square operation
Temporal pattern differs due to secret-dependent memory accesses
  Corresponds to bits in exponent
Used in both RSA and ElGamal decryptions

## Slide 17
0

## Slide 18
00

## Slide 19
001

## Slide 20
0011....

## Slide 21: The Good, The Bad...
The attack is practical, even with:
  Non-collocated cores
  No knowledge of any page table mappings (victim and attacker)
  No page-sharing between victim and attacker
No need to reverse the sliced cache hash function
Higher bandwidth than prior work (1.2Mb/s vs 190Kb/s)
In a real system, it is non-trivial to figure out what cache set maps to a particular part of the code
Requires information about the software artifact the victim is using
Experiments were run in isolation: real cloud will be noisier and harder to figure out

## Slide 22: ... and The Future (work)
With such an automatic side-channel detection build an automated tool for exploiting collocated clients
  Identify web services by measuring latency from inside the datacenter
  Extract keys from TLS negotiation
  (scare everyone in the process?)
Automatic detection of secret-dependent accesses
  Sample from a lot of known crypto libraries
  Train a model
  Attach a model to the attacker code, PRIME+PROBE the collocated clients continuously
Explore how the attack could extend to NUMA architectures
  Sounds hard: how to prime remote memory?